## Slide 1: AS91904 Electronics Outcome
Student Name: Heinrich venter Project Name:hybrid pitbike

## Slide 2: Project Details
Describe your project here: This project is a hybrid 70cc pit bike that combines a petrol engine with an 800 W, 36 V electric motor to improve low-speed torque and acceleration. An ESP32 uses analogue and digital Hall effect sensors to monitor throttle position and engine speed, then controls the electric motor through a motor controller. An electromagnetic clutch engages the motor only when assistance is needed, creating a hybrid drivetrain that combines mechanical and electronic systems.

## Slide 3: Techniques used
Technique 1: Implementing communication protocols
Evidence:
I will meet this requirement by using I2C communication to connect the ESP32 to the OLED dashboard display. This allows important information such as speed and RPM data to be transferred to the display while only using two communication pins, leaving the remaining pins available for other sensors and system components.
Technique 2: Filtering, noise and EMI suppression
Evidence:
I will meet this requirement by adding filtering components, such as 0.1µF ceramic capacitors, to reduce electrical noise caused by the high-current electric motor. This will improve the reliability of the Hall effect sensors, LED indicators, and battery monitoring system by providing more stable and accurate readings.
Techniques could be:
implementing communication protocols
Wireless transfer of information
Feedback control
Implementing software flags and interrupts
CAD design, 3D printing, CNC, PCB making
filtering, noise and EMI suppression.

## Slide 4: Relevant Implications
Description of Implication (What Where Why) | Explanation of Implication (How, Why) | Evidence of addressing.
Accessibility for the pitbike means the bike’s controls, indicators, and basic functions need to be understandable and manageable for a range of riders. This includes clear visual indicators, easy-to-reach switches, and controls that don’t require excessive strength. | It is important because riders need to operate the hybrid system, throttle, and display safely without confusion. I will address this by using clearly labelled switches, simple control layouts, and making sure components like the electric–petrol mode indicator are easy to read. | This was done by coding and producing a dashboard with 2 lines of leds one for the motor rpm and the other for the engine rpm to see when the clutch has to disengage and when the gear on the engine has to change as well as a Oled screen to see the speed of the bike as well as a second screen for sensor values so that troubleshooting can be done on the fly without needing a phone (for simpler usability)
Usability relates to how easy it is to understand and use the pitbike’s hybrid systems, such as switching modes, checking battery levels, or starting the bike. The design needs to feel intuitive even for new riders. | It matters because if the interface is confusing, the rider could misuse the bike or struggle during operation. I will address this by keeping the hybrid controls simple, limiting unnecessary switches, and providing a logical layout similar to standard pitbikes so it feels familiar. | Mapping the analogue throttle Hall sensors linearly alongside the petrol throttle, using software constraints (constrain(throttlePercent, 0, 100)).
Functionality refers to how well the 70cc hybrid pitbike performs its intended purpose—delivering reliable petrol and electric operation, smooth power delivery, and stable riding. It also includes ensuring the components (battery, controller, mechanical systems) work together correctly. | It is important because the bike must be reliable and safe. I will address this by testing the hybrid system regularly, checking wiring, ensuring the mechanical and electrical parts don’t interfere with each other, and confirming that power output remains stable. | Offloading sensor pulses to low-overhead interrupts (enginePulse, matchPulse, motorPulse), allowing the VCU to match shaft speeds before engaging the 24V clutch.
Aesthetics for the pitbike include the visual design—how the hybrid components are integrated, how tidy the wiring is, and the overall look of the bike. A clean, professional aesthetic helps the bike feel intentional rather than thrown together. | It is important because a well-presented bike improves user confidence and makes maintenance easier. I will address this by organising wiring neatly, using matching colours or covers, and ensuring added components blend with the original frame so the hybrid upgrade looks cohesive. | Consolidating loose jumper wires onto a custom dual-layer PCB enclosed in a watertight, form-fitting 3D-printed ABS structural housing shell.

## Slide 5: Original Design
Insert diagram here of electronics outcome
v
Made by ai

## Slide 6: Behaviour and function
The behaviour of the electronics is as follows.
Electric Motor Control
An analogue Hall effect sensor is used as the throttle input to send a signal to the 36 V motor controller, which controls the 800 W electric motor.
A 36 V to 12 V DC-DC buck converter is used to safely power the Arduino Uno R4 WiFi from the bike’s main battery system.
Hybrid Power Switching
A 24 V electromagnetic clutch is used to connect and disconnect the electric motor from the drivetrain.
Both the petrol engine and electric motor provide power during acceleration to improve low-speed torque.
At higher speeds, the electric motor disengages because the petrol engine can operate at a higher RPM.
A second Hall effect sensor is connected to the clutch lever, allowing the rider to manually disengage the electric motor when required.
RPM Matching System
Two digital Hall effect sensors measure the RPM on both sides of the electromagnetic clutch.
The Arduino uses this data to match the electric motor speed with the drivetrain before engaging the clutch, preventing drivetrain damage and sudden speed changes.

## Slide 7
Speed Monitoring
A digital Hall effect sensor mounted near the rear wheel measures wheel rotation speed.
The Arduino calculates the bike’s speed and displays it on the dashboard.
Dashboard Display
An OLED display and LED indicators provide the rider with real-time information.
The dashboard displays:
Vehicle speed
Engine RPM
Electric motor RPM
Battery percentage

## Slide 8: Explaining relevant communication protocols
I am using I2C communication between the ESP32and the OLED dashboard display. I2C works by using two communication lines: SDA (Serial Data) to transfer information and SCL (Serial Clock) to synchronise the data transfer. The Arduino acts as the master device, sending information to the OLED display, which acts as the slave device. This allows the system to display real-time information such as speed, RPM, and battery voltage.
I selected I2C because it only requires two Arduino pins, leaving more available pins for the other sensors used in the bike, such as Hall effect sensors and RPM sensors. I2C also provides enough communication speed for a small OLED display while allowing additional devices to be added to the same communication bus in the future.

## Slide 9: Iterated Design
Feedback:
Made by ai

## Slide 10: Components and Systems

## Slide 11: Choice of Component/System 1: controller
Justification of choice made
I chose the esp32 for its native wifi and Bluetooth capabilities aswell as its increased gpio pins compared to other boards, another reason is that it is faster at reading sensor readings
Chosen
ESP32-s3
Alternative 1
Arduino r4 wifi
Alternative 2
Arduino r3

## Slide 12: Component/System 1
Explanation of component-brain
The ESP32 is the main microcontroller used in my project. It is a microcontroller with a wifi component onboard meaning it can be controlled wirelessly using wifi, it also has gpio pins on the side so that sensors and components like a PCB can be added for adding more components
Component Picture
Component test log:

## Slide 13: Reliability Testing
Analyse notes from testing and note changes to be made:
Multiple test
Reliability notes from testing:

## Slide 14: Choice of Component/System 2:physical controls
Justification of choice made
The reason why I chose the hall effect sensor is due to simplicity and the fact that it use magnets for signal input meaning nothing is touching so no friction and near zero wear in the parts, it is also very easy to make a custom casing for it to be held in place where ever its needed
Chosen
Hall effect sensor
Alternative 1
Potentiometer
Alternative 2
optical encoder

## Slide 15: Component/System 2
Explanation of component-speed/rpm sensing
The speed and RPM tracking system uses digital Hall effect sensors with neodymium magnets attached to the rotating parts of the bike, including the clutches and rear wheel. When the magnet passes the sensor, it detects the change in the magnetic field and sends a digital signal (0V or 5V) to the Arduino. These signals are used by the Arduino to calculate the RPM of the drivetrain and the speed of the bike by measuring the time between each pulse.
Component Picture
Component Test Log: there is a bit of electromagnetic interference from other magnets like the clutch and the engine, adding a 0.1uf capacitor across the signal and gnd wires did reduce this emi

## Slide 16: Reliability Testing
Analyse notes from testing and note changes to be made: twisting the 3 wires ontop of eachother which creates an inductor which resist signal roughness
Multiple test
Reliability notes from testing: the analog hall sensors still have a little bit of bounce to its signal but still readable tho

## Slide 17: Choice of Component/System 3
Justification of choice made
The chosen 1.3" I2C OLED display was selected because it provides a clear and efficient way to display information from the ESP. It is not only bright enough to be seen in the day but only uses 4 wires (gnd, 3v3, sda and scl) (scl:serial clock sda: serial data) wich is also very easy to programme and controll
Chosen
1.3” i2c Oled screen
Alternative 1
Lcd screen
Alternative 2
SPI TFT colour display

## Slide 18: Component/System 3
Explanation of component-dashboard:The dashboard provides the rider with a real-time visual interface displaying operational telemetry. It features a 1.3" SH1106 I2C OLED display running in tandem with a custom 16-LED tachometer bar driven by an MCP23017 port expander.
Component Picture
Component Test Log:

## Slide 19: Reliability Testing
Analyse notes from testing and note changes to be made:
to prevent environmental short circuits, I designed a sealed handlebar mounting dashboard cluster using 3D-printed PETG. I integrated a transparent acrylic faceplate and cut a custom, shock-absorbing TPU gasket to seal the electronics safely away from weather exposure.
Multiple test
Reliability notes from testing:

## Slide 20: Choice of Component/System 4
Justification of choice made
I chose the electromagnetic clutch because, when a electric motor gets back driven it can cause something called back emf which is basically electric breaking but with a electromagnetic clutch yon can physically disconnect the 2 power units from each other specifically the electric motor which mean no back emf.
Chosen
Electromangetic clutch
Alternative 1
Automatic Centrifugal Clutch Mechanism.
Alternative 2
One way bearing

## Slide 21: Component/System 4
Explanation of component-electromagnetic clutch
The clutch system is used to connect and disconnect the 800W electric motor from the drivetrain. It uses a mechanical clutch mechanism controlled by a lever, with a sensor attached to detect when the clutch is being used. When the rider pulls the lever, the clutch disengages the motor from the drivetrain, allowing the motor to be safely disconnected. The sensor sends this information to the Arduino, allowing it to stop motor assistance and adjust the system accordingly.
Component Picture
Component Test Log: The purpose of this test was to check that the manual clutch could reliably engage and disengage the 800W motor from the drivetrain. The clutch was connected to the motor system and tested under load to ensure it could separate the drive components correctly. Initial testing showed some resistance in the lever mechanism, causing the clutch plates to separate slowly. The linkage was cleaned, adjusted, and lubricated to fix this issue. After these changes, the clutch successfully completed ten engagement and disengagement tests without slipping, confirming that it worked correctly.

## Slide 22: Reliability Testing
Analysis Notes from Testing and Changes to be Made: Testing showed that the high torque produced by the 800W motor puts significant load on the clutch assembly, making correct alignment important for reliable operation. Small amounts of misalignment can cause extra stress and increased wear on the drivetrain components. To improve the strength and reliability of the system, a custom sleeve will be manufactured to act as a central alignment piece. This will help keep the clutch and drivetrain components correctly positioned, reducing movement and improving long-term durability.
Test your circuits at least 10 times
Reliability notes from testing:
Manual clutch assembly stress trials revealed initial instability and wobble, which were corrected by manually aligning the central hub to ensure proper clearance. Following this adjustment, the system demonstrated consistent, reliable performance throughout the remaining tests without mechanical failure.

## Slide 23: Choice of Component/System 5
Justification of choice made
I chose a custom PCB because it gave me a cleaner and more reliable way of connecting all the electronics together. The PCB allowed me to place the Arduino, sensors, protection components and other circuits in one organised layout instead of having lots of separate wires. This was especially important because testing showed that electrical noise from the motor could affect the sensors. A PCB also made the final system more compact and reduced the chance of loose or incorrect connections.
I considered perfboard and stripboard, but both would have required more manual wiring and would have been harder to keep organised. The PCB was also easier to reproduce once the design was finished, making it the better choice for the final outcome.
Chosen
PCB
Alternative 1
Perfboard
Alternative 2
Strip boards

## Slide 24: Component/System 5
Explanation of component-PCB I designed a custom PCB to connect the Arduino UNO R4 to the different sensors and circuits used on the bike. It includes connections for the throttle and clutch Hall sensors, RPM sensors, battery voltage sensing, LEDs and the protection circuits. Having these connections on one board made the wiring cleaner and reduced the number of separate wires and connections. I also included filtering capacitors and protection components on the PCB based on problems found during testing. This made the final electronics more compact, organised and reliable.
Component Picture
Component Test Log: make sure to include protection to the circuit due to some components accidently being set to the wrong voltage can damage the delicate electronics in the system that when it gets damaged can cost a pretty penny to replace

## Slide 25: Reliability Testing
Analysis Notes from Testing and Changes to be made: The testing showed that the PCB needed both filtering and protection to be reliable when used with the rest of the bike. The 0.1 µF capacitors were added to reduce electrical noise, while the PPTC fuses gave the PCB protection from excessive current if a fault occurred. The Schottky diode was added to the clutch circuit to stop the voltage released by the electromagnet from travelling back through the PCB. These changes were made from the problems found during testing and improved the reliability of the final PCB by making the circuits more protected and less affected by the electrical noise from the motor.
Test your circuits at least 10 times
Reliability notes from testing: I tested the PCB multiple times with the different circuits connected to make sure the board was reliable. I checked the sensor connections, battery voltage sensing, Arduino power connections and the protection circuits. During testing, I found that the high current from the motor could cause electrical noise and interference with the sensor signals, so 0.1 µF capacitors were added to the PCB to help filter the signals. I also included PPTC fuses on the PCB to protect the lower-current circuits if a fault or short circuit occurred. The electromagnetic clutch circuit was also protected with a Schottky diode and PPTC because testing showed that the electromagnet could release a high voltage back into the circuit when switched off. The PCB was then tested again with these changes to check that the sensors and protection circuits were working correctly and that the board could operate without damaging the Arduino or other components.

## Slide 26: Final Outcome, Before Testing
Include a screenshot/video of the final outcome working before testing here

## Slide 27: Iteration of Development
Feedback on reliability and functionality of the system:
Some hybrid vehicles have a display that shows when the hybrid system is engaged. Adding a hybrid indicator light to the pitbike will let the rider know when the electric motor is assisting the petrol engine. This provides feedback that the hybrid system is working correctly and makes it easier to monitor the operation of the bike while riding.
Changes based off feedback (include picture or design):
An LED indicator/symbol will be added to the OLED display to show when the hybrid system is engaged. This gives the rider clear visual feedback that the electric motor is assisting the petrol engine and makes it easier to monitor the operation of the hybrid system while riding.

## Slide 28: Testing and Debugging

## Slide 29: Testing for functionality
Project Specification | Test | Issues to be fixed, debugging, Notes
Electromagnetic clutch | Repeatedly engaged and disengaged the clutch using the Arduino and MOSFET. | Clutch engaged reliably but mechanical alignment needed improvement. Designed a custom sleeve to keep the clutch centred.
main PCB inside the dashboard | Plugged the PCB wit the Arduino inserted to the header pins. The Arduino fried due to unknown causes for the vin wasn’t plugged in and neither the voltage sensing, believed being the sensor wire for the throttle but in any case, it still broke. | Adding PPTC fuses to the vin, voltage sensing, buck converters, electromagnet. A automotive fuse to the motor and a main automotive fuse for all the pcb and buck converters (max 5Amps). Also adding diodes to the battery electromagnet vin, voltage sensing, and Mosfet to protect every component from back voltage and incorrect wiring
Throttle input/output |  | 
Examples of testing, modifying and debugging include: using testing devices and testing strategies, testing expected, boundary and invalid inputs, changing board layout, improving component selection. You may test as you go

## Slide 30: Testing for reliability
Potential problem, original reliability | Test and change for reliability | Issues to be fixed, debugging, Notes
Electrical interference from the 800 W motor could cause false Hall sensor readings. | The Hall effect sensors were tested while the motor was running under load. A 0.1 uF ceramic capacitor was added across the signal and ground lines to reduce electrical noise before repeating the test. | Before the capacitor was fitted, false RPM readings occasionally occurred. After retesting, the sensor produced stable and reliable readings with no false triggers.
The electromagnet releases a huge amount of voltage back into the system when it get turn off | 3 diodes and a fuse were added to the system , a Schottky, Zener and TVS diode and a PPTC fuse(Polymeric Positive Temperature Coefficient fuse) these are to protect the circuits from over voltage and back Volting the system preventing the system from going up in smoke, they were tested by turning the magnet on and off and applying a multimeter to the circuits end points and seeing if there is a over voltage that that part gets shut down (the part that is being measured) | Make sure the right rated diodes and PPTC fuses are used for the right circuits Don’t use a PPTC fuse on the motor use a automotive fuse so that it will completely shut the motor off if it pulling to many amps Test all the endpoints before attaching delicate and expensive components

## Slide 31: Iteration after testing
Feedback after testing:
Changes based off feedback (include picture or design):