## Slide 1: AS91904 Electronics Outcome
Student Name: Heinrich venter Project Name: Mark Sutherland

## Slide 2: Project Details
Describe your project here:

## Slide 3: Techniques used
Technique 1: Implementing communication protocols
Evidence:
Technique 1:
Evidence:
Techniques could be:
implementing communication protocols
Wireless transfer of information
Feedback control
Implementing software flags and interrupts
CAD design, 3D printing, CNC, PCB making
filtering, noise and EMI suppression.

## Slide 4: Relevant Implications
Description of Implication (What Where Why) | Explanation of Implication (How, Why) | Evidence of addressing.
Accessibility for the pitbike means the bike’s controls, indicators, and basic functions need to be understandable and manageable for a range of riders. This includes clear visual indicators, easy-to-reach switches, and controls that don’t require excessive strength. | It is important because riders need to operate the hybrid system, throttle, and display safely without confusion. I will address this by using clearly labelled switches, simple control layouts, and making sure components like the electric–petrol mode indicator are easy to read. | 
Usability relates to how easy it is to understand and use the pitbike’s hybrid systems, such as switching modes, checking battery levels, or starting the bike. The design needs to feel intuitive even for new riders. | It matters because if the interface is confusing, the rider could misuse the bike or struggle during operation. I will address this by keeping the hybrid controls simple, limiting unnecessary switches, and providing a logical layout similar to standard pitbikes so it feels familiar. | 
Functionality refers to how well the 70cc hybrid pitbike performs its intended purpose—delivering reliable petrol and electric operation, smooth power delivery, and stable riding. It also includes ensuring the components (battery, controller, mechanical systems) work together correctly. | It is important because the bike must be reliable and safe. I will address this by testing the hybrid system regularly, checking wiring, ensuring the mechanical and electrical parts don’t interfere with each other, and confirming that power output remains stable. | 
Aesthetics for the pitbike include the visual design—how the hybrid components are integrated, how tidy the wiring is, and the overall look of the bike. A clean, professional aesthetic helps the bike feel intentional rather than thrown together. | It is important because a well-presented bike improves user confidence and makes maintenance easier. I will address this by organising wiring neatly, using matching colours or covers, and ensuring added components blend with the original frame so the hybrid upgrade looks cohesive. | 

## Slide 5: Original Design
Insert diagram here of electronics outcome

## Slide 6: Behaviour and function
The behaviour of the electronics is as follows. Firstly to relay signal to a motor controller for the 800w electric motor which is done with a analog hall effect sensor, the reason for having a separate controller is because the motor runs on 36v where as the Arduino r4 runs on 12v which is done with a 36-12v dc-dc buck converter. The next part is to have the 2 power units be separatable, this is done with a 24v electromagnetic hall effect sensor and another analog hall effect sensor so that when the bike comes offthe line both units are giving power and when the bike reaches a certain speed the clutch will disengage the electric motor from the engine(this is because the engine can go at a much greater rpm comparted to the electric motor) also in the case that I need the motor detached from the rest of the power train I have the analog hall effect sensor connected to the clutch leaver so that when I pull in the clutch It disengages both clutches. The third is the rpm sensing so using 2 digital hall effect sensors so detect therpm of both sides of the clutch so that before the magnetic clutch engages (since it will be disengaged at higher speeds) the electric motor matches the speed of the rest of the drive train otherwise if it doesn’t and it is slower than the rest of the drive train it can either cause the bike to go slower or caused catastrophic damage to the bike itself. The fourth is the speed sensing using a digital hallleffecct sensor attached to the rear wheel to tell the Arduino what speed the bike is traveling at. Fithly battery and fuel gauges for the battey using a capacitor and resistor to give a readable signal for the Arduino to show the voltage of the battery and for the fuel using a flow sensor to tell the Arduino if there is fuel flow in the fuel lines so if there isn’t that means the fuel is low Lastly is the dashboard so using a Oled display and a few led’s to visually display the speed, the rpm and the battery and fuel percentage.

## Slide 7: Explaining relevant communication protocols
For this project, I am using the I2C (Inter-Integrated Circuit) communication protocol to interface the Arduino with the dashboard OLED display. I2C operates as a master-slave system using a two-wire synchronous bus consisting of a Serial Data line (SDA) and a Serial Clock line (SCL). The Arduino acts as the master device, generating the clock signal and initiating contact by transmitting the unique 7-bit hardware address belonging to the OLED display. Once communication is established, the Arduino uses this data bus to send continuous, real-time telemetry updates. Specifically, I am using this protocol to transmit calculated values ​​for the e-bike's speed, clutch RPM, battery voltage, and fuel flow status directly to the screen for the rider to see.
I selected the I2C protocol over alternative methods because it offers the best balance between speed and pin efficiency for this specific sensor-heavy application. While alternative interfaces like Parallel require eight or more digital pins, and SPI requires four, I2C requires only two microcontroller pins. Minimizing pin usage is critical for this e-bike layout because the system demands numerous dedicated hardware inputs for the digital speed sensors, analog clutch sensors, and the fuel flow meter. While SPI offers faster data transfer rates than I2C, the extra bandwidth is unnecessary for updating a small, primarily text-based dashboard screen. Furthermore, I2C supports multi-device connectivity on the same bus, allowing future upgrades—such as adding an I2C accelerometer or telemetry module—without consuming any additional physical pins on the Arduino.

## Slide 8: Iterated Design
Feedback:
Insert updated diagram here of electronics outcome

## Slide 9: Components and Systems

## Slide 10: Choice of Component/System 1: controller
Justification of choice made
I chose the Arduino r4 over the esp 32 because is have a fundamental uderstranding on the workings of the arduios compared to a the esp32 which ive never used before. I chose the r4 over the r3 because the r4 has a wifi chip on board which means that I can made a ui to adjust settings like throttle logic and sensitivity and when I need to do maintenance I can turn stuff of like the clutch for example
Chosen
Ardunio R4
Alternative 1
Esp 32
Alternative 2
Arduino r3

## Slide 11: Component/System 1
Explanation of component
The Arduino UNO R4 WiFi is a powerful 32-bit development board that combines a Renesas RA4M1 ARM Cortex-M4 processor with an Espressif ESP32-S3 module for Wi-Fi and Bluetooth connectivity. It retains the classic UNO footprint and 5V logic, making it ideal for both beginners and advanced IoT projects.
Component Picture
Component test log: very easy to control and upload code through a cable but still working on the uploading over wifi.

## Slide 12: Reliability Testing
Analyse notes from testing and note changes to be made: through feedback ive found that incorporating a 0.1uf capacitor across the signal and ground wires of the sensors it can smoot the signal out to a very clear and stable signal, adding a 1k resisitor to the leds can make it slightly dimmer and can also make its longevity of the leds much greater cause the heat is greatly decreased, meaning that the chance of it blowing goes down cause the voltage is decreased that goes to the led itself
Test your circuits at least 10 times
Reliability notes from testing: the analog hall sensors have a very jumpy signal

## Slide 13: Choice of Component/System 2
Justification of choice made
The chosen 1.3" I2C OLED display is the optimal choice for this system as it balances pixel-level graphic control (128x64 resolution) with high efficiency, vastly outperforming Alternative 1 (LCD screen) , which is limited to rigid character blocks, requires a high-draw backlight, and offers poor viewing angles. Because OLED pixels are self-emissive, unlit black pixels consume virtually zero power, making it ideal for low-power microcontrollers deployment. Additionally, while Alternative 2 (1.8" SPI TFT Color Display) provides vibrant colors, its SPI interface requires 4 to 5 data pins, which limits available inputs and complicates wiring. In contrast, the chosen OLED uses the I2C protocol , requiring only two shared lines (SDA and SCL). This preserves critical GPIO pins for other sensors, simplifies breadboard layout, and ensures a compact, power-efficient, and easily scalable system architecture.
Chosen
1.3” i2c Oled screen
Alternative 1
Lcd screen
Alternative 2
1.8” SPI TFT colour display

## Slide 14: Component/System 2
Explanation of component
The speed and RPM tracking subsystem utilizes digital Hall effect sensors paired with neodymium magnets mounted on the rotating shafts (the clutches and the rear wheel). As the components spin, the magnet passes the face of the sensor, causing a state change in the magnetic field that triggers the sensor to output a clean digital pulse (switching between 0V and 5V). These sensors are wired directly to the Arduino's hardware interrupt pins. The microcontroller tracks the time interval between these incoming digital pulses to accurately calculate the real-time rotational speed (RPM) and the physical travel speed of the electric bike.
Component Picture
Component test log:
0.1uf smoothing capacitor was integrated across the signal and ground lines, which successfully filtered out the raw signal noise and stabilized the voltage drops. Following this hardware optimization, the Arduino recorded clean, reliable signal transitions with zero missed pulses or false triggers, confirming a successful PASSED status for the subsystem.

## Slide 15: Reliability Testing
Analyse notes from testing and note changes to be made:0.1uf ceramic capacitor will be permanently soldered onto the PCB layout as close to the sensor input pins as possible to act as a permanent low-pass filter. Additionally, future iterations will utilize shielded twisted-pair cabling for all external sensor runs to provide structural immunity against external vehicle engine noise.
Test your circuits at least 10 times
Reliability notes from testing:0.1uf hardware decoupling capacitor between the signal line and ground before trial 5, the data stabilized immediately. Across the remaining 6 trials, the sensor delivered a completely uniform, repeatable pulse train with zero false triggers, maintaining an identical, steady tracking waveform across all final iterations.

## Slide 16: Choice of Component/System 3
Justification of choice made
The custom resistor voltage divider circuit was chosen because it provides the most elegant, cost-effective, and accurate solution for scaling down the battery's high voltage to a safe 0-5v level for the Arduino. Alternative 1 (a pre-built analog sensor module) was rejected because it simply uses the same basic resistor divider network but takes up significantly more physical space on the chassis and adds unnecessary manufacturing costs. Alternative 2 (a dedicated digital I2C ADC module) offers incredibly high bit resolution, but it is entirely unnecessary for this application since the Arduino’s built-in 10-bit ADC provides more than enough precision to read a standard vehicle battery level accurately. By choosing a custom resistor network paired with a 0.1uf filtering capacitor, the circuit minimizes bulk component footprints, eliminates the need for complex external software libraries, and directly cleans out high-frequency noise from heavy motor draw at a fraction of the cost of commercial modules.
Chosen
Resistor Voltage Divider Circuit with a 0.1 uf filtering capacitor
Alternative 1
Dedicated Analog Voltage Sensor Module (eg, ZMPT101B or standard voltage sensor breakout).
Alternative 2
Digital I2C Analog-to-Digital Converter (ADC) Module (eg, ADS1115 breakout).

## Slide 17: Component/System 3
Explanation of component
The fuel flow monitoring subsystem is designed to detect and measure the presence of fuel moving through the e-bike's line inputs using a digital turbine flow sensor. Inside the sensor, a tiny pinwheel turbine spins as liquid passes through it, which triggers an internal magnetic Hall effect switch to output a continuous train of digital frequency pulses. The Arduino reads these incoming high/low pulses via a digital input pin using a hardware interrupt. By counting the number of pulses received over a precise time interval, the microcontroller applies a calibration factor in the code to calculate the real-time flow rate, which is then sent to the OLED display to track fuel line health and usage.
Component Picture
Component test log:
The objective of this test was to verify that the digital fuel flow sensor outputs stable frequency pulses proportional to fluid movement and that the Arduino accurately processes these transitions without signal loss. The sensor was integrated into a test-bench loop where a controlled volume of liquid was passed through the turbine housing while the output signal was tracked via an Arduino digital interrupt pin. Initial trials showed clean pulse generation, but nearby high-power components from the 800W motor introduced electrical noise that caused minor counting anomalies. To resolve this, a 01 uf capacitor was added to the signal line to filter out the high-frequency interference. Across ten consecutive test cycles passing a calibrated volume of 500mL, the Arduino consistently recorded accurate, steady volumetric data within an acceptable +-5% tolerance, successfully confirming a PASSED testing status.

## Slide 18: Reliability Testing
Analyse notes from testing and note changes to be made:
Data analysis indicates that heavy current draw from the 800W motor creates massive magnetic fields that easily corrupt the delicate pulse trains generated by the flow sensor's internal Hall switch. Relying on software corrections alone cannot fix this real-time electrical noise. To guarantee long-term system reliability on the road, two permanent changes will be implemented: first, a 0.1uf filtering capacitor will be permanently soldered directly onto the interface circuit board to suppress high-frequency spikes. Second, the sensor run will be rewired using braided, grounded shield cables to completely isolate the fluid tracking signals from the bike's main power lines.
Test your circuits at least 10 times
Reliability notes from testing:
To verify the physical and electrical endurance of the fuel flow sensor system under active riding conditions, the circuit was subjected to a rigorous series of 10 consecutive fluid-flow trials. In the first 3 trials, the system reported erratic volume drops and false pulse counts whenever the nearby 800W motor was revved, proving that unshielded sensor lines were highly vulnerable to electromagnetic noise. Prior to trial 4, a 0.1uf hardware decoupling capacitor was installed across the signal line, and the sensor wiring was routed away from the high-voltage motor cables. Across the remaining 7 test cycles, the output data stabilized completely, delivering completely uniform, repeatable flow tracking with a stable pulse frequency and zero data drops.

## Slide 19: Choice of Component/System 4
Justification of choice made
+-1% 5Vdigital pulse output for the Arduino, and delivers reliable, rock-steady volumetric readings that remain unaffected by fluid density changes.
Chosen
G1/4" SEA OF07ZAT Oval Gear Digital Flow Meter.
Alternative 1
Standard Plastic Turbine Liquid Flow Sensor (eg, YF-S201).
Alternative 2
Differential Pressure Fuel Flow Transducer.

## Slide 20: Component/System 4
Explanation of component
The fuel flow monitoring subsystem utilizes an OF07ZAT G1/4" oval gear flow sensor to accurately measure liquid moving through the e-bike's line inputs. Unlike standard turbine sensors, this component uses two high-precision, meshing oval gears that are pushed by the fluid's pressure, providing positive displacement that allows it to measure thick or viscous fluids like diesel and oils with high precision. As these oval gears rotate, internal magnets pass a built-in Hall effect switch, generating a clean digital pulse train. The Arduino reads these high/low pulses via a digital hardware interrupt pin, counting the frequency of the pulses over time to calculate the exact, real-time volumetric flow rate for the rider's OLED dashboard display.
Component Picture
Component test log:
The objective of this test was to verify that the OF07ZAT oval gear sensor outputs stable digital frequency pulses proportional to fluid movement and that the Arduino accurately processes the data without losing counts. The sensor was plumbed into a test loop using a calibrated volume of fluid while its signal pin was monitored via an Arduino digital interrupt input. Initial runs showed consistent gear rotation, but high-frequency electrical noise from the nearby 800W motor caused minor counting anomalies on the microchip. To completely isolate the signal, a 0.1uf capacitor was added across the signal and ground lines to act as a hardware low-pass filter. Following this hardware modification, the system passed ten consecutive test iterations of a 500mL fluid run with an outstanding volumetric accuracy within+-1%, successfully achieving a PASSED calibration status.

## Slide 21: Reliability Testing
Analyse notes from testing and note changes to be made:
Analysis of the testing logs indicates that heavy current draw from the 800W motor creates massive magnetic fields that easily corrupt the delicate digital pulse trains generated by the flow meter's internal Hall switch. Relying on software corrections alone cannot filter out this real-time electrical noise. To guarantee long-term system reliability on the vehicle, two permanent hardware changes will be implemented: first, a 0.1uf ceramic filtering capacitor will be permanently soldered directly onto the interface circuit board to suppress high-frequency voltage spikes. Second, the sensor run will be rewired using braided, grounded shield cables to completely isolate the fluid tracking signals from the bike's main power lines.
Test your circuits at least 10 times
Reliability notes from testing:
To verify the physical and electrical endurance of the volumetric tracking system under active riding conditions, the OF07ZAT sensor circuit was run through a sequence of 10 consecutive fluid-flow trials. During the first 3 trials, the system reported erratic volume jumps and unstable pulse counts whenever the nearby 800W motor was operated at high loads, proving that unshielded sensor lines were highly vulnerable to electromagnetic noise. Prior to trial 4, a 0.1uf hardware decoupling capacitor was installed across the signal line, and the sensor wiring layout was physically isolated from the high-voltage motor cables. Across the remaining 7 test cycles, the data stabilized completely, delivering a perfectly uniform, repeatable pulse train with zero missed gear rotations or false data drops.

## Slide 22: Final Outcome, Before Testing
Include a screenshot/video of the final outcome working before testing here

## Slide 23: Iteration of Development
Feedback on reliability and functionality of the system:
Changes based off feedback (include picture or design):

## Slide 24: Testing and Debugging

## Slide 25: Testing for functionality
Project Specification | Test | Issues to be fixed, debugging, Notes
Examples of testing, modifying and debugging include: using testing devices and testing strategies, testing expected, boundary and invalid inputs, changing board layout, improving component selection. You may test as you go

## Slide 26: Testing for reliability
Potential problem, original reliability | Test and change for reliability | Issues to be fixed, debugging, Notes

## Slide 27: Iteration after testing
Feedback after testing:
Changes based off feedback (include picture or design):